## Slide 1: Basics of Boolean Algebra

## Slide 2: Binary Logic and Gates
Binary variables take on one of two values.
Logical operators operate on binary values and binary variables.
Basic logical operators are the logic functions AND, OR and NOT.
Logic gates implement logic functions.
Boolean Algebra: a useful mathematical system for specifying and transforming logic functions.
We study Boolean algebra as a foundation for designing and analyzing digital systems!

## Slide 3: Binary Variables
Recall that the two binary values have different names:
  True/False
  On/Off
  Yes/No
  1/0
We use 1 and 0 to denote the two values.
Variable identifier examples:
  A, B, y, z, or X1 for now
  RESET, START_IT, or ADD1 later

## Slide 4: Logical Operations
The three basic logical operations are:
  AND
  OR
  NOT
AND is denoted by a dot (·).
OR is denoted by a plus (+).
NOT is denoted by an overbar ( ¯ ), a single quote mark (') after, or (~) before the variable.

## Slide 5: Notation Examples
Examples:
  is read “Y is equal to A AND B.”
  is read “z is equal to x OR y.”
  is read “X is equal to NOT A.”
Note: The statement:
  1 + 1 = 2 (read “one plus one equals two”)
is not the same as
  1 + 1 = 1 (read “1 or 1 equals 1”).
=
B
A
Y
×
y
x
z
+
=
A
X
=

## Slide 6: Operator Definitions
Operations are defined on the values "0" and "1" for each operator:
AND
0 · 0 = 0
0 · 1 = 0
1 · 0 = 0
1 · 1 = 1
OR
0 + 0 = 0
0 + 1 = 1
1 + 0 = 1
1 + 1 = 1
NOT
1
0
=
0
1
=

## Slide 7: Truth Tables
0
1
1
0
X
NOT
X
Z
=
Truth table - a tabular listing of the values of a function for all possible combinations of values on its arguments
Example: Truth tables for the basic logic operations:
1
1
1
0
0
1
0
1
0
0
0
0
Z = X·Y
Y
X
AND
OR |  | 
X | Y | Z = X+Y
0 | 0 | 0
0 | 1 | 1
1 | 0 | 1
1 | 1 | 1

## Slide 8: Logic Function Implementation
Using Switches
  For inputs:
    logic 1 is switch closed
    logic 0 is switch open
  For outputs:
    logic 1 is light on
    logic 0 is light off.
  NOT uses a switch such
  that:
    logic 1 is switch open
    logic 0 is switch closed
Switches in series => AND
Switches in parallel => OR

## Slide 9: Logic Function Implementation (Continued)
Example: Logic Using Switches
Light is on (L = 1) for
  L(A, B, C, D) = ?
  and off (L = 0), otherwise.
B
A
D
C
Notes: L (A, B, C, D) = A ((B C') + D) = A B C' + A D

## Slide 10: Logic Gate Symbols and Behavior
Logic gates have special symbols:
And waveform behavior in time as follows:

## Slide 11: Buffer
A buffer is a gate with the function F = X:
In terms of Boolean function, a buffer is the same as a connection!
So why use it?
  A buffer is an electronic amplifier used to improve circuit voltage levels and increase the speed of circuit operation.
X
F

## Slide 12: NAND Gate
The basic NAND gate has the following symbol, illustrated for three inputs:
  AND-Invert (NAND)
NAND represents NOT AND, i. e., the AND function with a NOT applied. The symbol shown is an AND-Invert. The small circle (“bubble”) represents the invert function.
The NAND gate is a universal gate
X
Y
Z
Z
Y
X
)
Z
,
Y
,
X
(
F
×
×
=

## Slide 13: NOR Gate
The basic NOR gate has the following symbol, illustrated for three inputs:
  OR-Invert (NOR)
NOR represents NOT - OR, i. e., the OR function with a NOT applied. The symbol shown is an OR-Invert. The small circle (“bubble”) represents the invert function.
The NOR gate is a universal gate
X
Y
Z
Z
Y
X
)
Z
,
Y
,
X
(
F
+
+
=

## Slide 14: Implement AND, OR, NOT using NAND

## Slide 15: Implement AND, OR, NOT using NOR

## Slide 17: Exclusive OR/ Exclusive NOR
The eXclusive OR (XOR) function is an important Boolean function used extensively in logic circuits.
The eXclusive NOR function is the complement of the XOR function

## Slide 18: Exclusive OR/ Exclusive NOR
Uses for the XOR and XNORs gate include:
  Adders/subtractors/multipliers
  Counters/incrementers/decrementers
  Parity generators/checkers
Definitions
  The XOR function is:
  The eXclusive NOR (XNOR) function, otherwise known as equivalence is:
Y
X
Y
X
Y
X
+
=
Å
Y
X
Y
X
Y
X
+
=
Å

## Slide 19: Truth Tables for XOR/XNOR
Operator Rules: XOR XNOR
The XOR function means:
X OR Y, but NOT BOTH
Why is the XNOR function also known as the equivalence function, denoted by the operator 
X
Y
X
Å
Y
0
0
0
0
1
1
1
0
1
1
1
0
X
Y
0
0
1
0
1
0
1
0
0
1
1
1
or X
º
Y
(X
Å
Y)
Notes: Because it is defined as X Y + X’ Y’ that equals 1 if and only if X = Y implying X is equivalent to Y.

## Slide 20: Symbols For XOR and XNOR
XOR symbol:
XNOR symbol:

## Slide 21: Gate Delay
In actual physical gates, if one or more input changes causes the output to change, the output change does not occur instantaneously.
The delay between an input change(s) and the resulting output change is the gate delay denoted by tG:
tG
tG
Input
Output
Time (ns)
0
0
1
1
0
0.5
1
1.5
tG = 0.3 ns

## Slide 22: Logic Diagrams and Expressions
Boolean equations, truth tables and logic diagrams describe the same function!
Truth tables are unique; expressions and logic diagrams are not. This gives flexibility in implementing functions.
X
Y
F
Z
Logic Diagram
Equation
Z
Y
X
F
+
=
Truth Table
1
1 1 1
1
1 1 0
1
1 0 1
1
1 0 0
0
0 1 1
0
0 1 0
1
0 0 1
0
0 0 0
X Y Z
Z
Y
X
F
×
+
=

## Slide 23: Boolean Algebra
1.
3.
5.
7.
9.
11.
13.
15.
17.
Commutative
Associative
Distributive
DeMorgan
’
s
2.
4.
6.
8.
X
. 1
X
=
X
. 0
0
=
X . X
X
=
0
=
X . X
An algebraic structure defined on a set of at least two elements, B, together with three binary operators (denoted +, · and ) that satisfies the following basic identities:
10.
12.
14.
16.
X + Y
Y + X
=
(X + Y)
Z
+
X + (Y
Z)
+
=
X(Y +
Z)
XY
XZ
+
=
X + Y
X . Y
=
XY
YX
=
(XY)
Z
X(Y
Z)
=
X
+ YZ
(X + Y)
(X + Z)
=
X . Y
X + Y
=
X
+ 0
X
=
+
X
1
1
=
X + X
X
=
1
=
X + X
X = X

## Slide 24: Boolean Operator Precedence
The order of evaluation in a Boolean expression is:
1.
Parentheses
2.
NOT
3.
AND
4.
OR
Consequence: Parentheses appear around OR expressions
Example: F = A(B + C)(C + D)

## Slide 25: Example 1: Boolean Algebraic Proof
A + A·B = A (Absorption Theorem)
Proof Steps Justification (identity or theorem)
A + A·B
= A · 1 + A · B X = X · 1
= A · ( 1 + B) X · Y + X · Z = X ·(Y + Z)(Distributive Law)
= A · 1 1 + X = 1
= A X · 1 = X
Our primary reason for doing proofs is to learn:
  Careful and efficient use of the identities and theorems of Boolean algebra, and
  How to choose the appropriate identity or theorem to apply to make forward progress, irrespective of the application.

## Slide 26: Useful Theorems
x
y
×
y
(
)
(
)
n
inimizatio
M
y
y
y
x
y
y
y
x
=
+
+
=
×
×
(
)
tion
Simplifica
y
x
y
x
y
x
y
x
×
=
+
×
+
=
×
+
Consensus
z
y
x
z
y
z
y
x
×
+
×
=
×
+
×
+
×
(
)
(
)
(
)
(
)
(
)
z
y
x
z
y
z
y
x
+
×
+
=
+
×
+
×
+
Laws
s
DeMorgan'
x
x
×
=
+
+
x
x
x
x
x
x
x
x
y
x
=
+
y

## Slide 27: Expression Simplification
+
+
+
+
D
C
B
A
D
C
A
D
B
A
D
C
A
B
A

## Slide 28: Expression Simplification
An application of Boolean algebra
Simplify to contain the smallest number of literals (complemented and uncomplemented variables):
= AB + ABCD + A C D + A C D + A B D
= AB + AB(CD) + A C (D + D) + A B D
= AB + A C + A B D = B(A + AD) +AC
= B (A + D) + A C 5 literals
+
+
+
+
D
C
B
A
D
C
A
D
B
A
D
C
A
B
A

## Slide 29: Complementing Functions
Use DeMorgan's Theorem to complement a function:
  1. Interchange AND and OR operators
  2. Complement each constant value and literal
Example: Complement F =
F = (x + y + z)(x + y + z)
Example: Complement G = (a + bc)d + e
G =
x
+
z
y
z
y
x
Notes: G' = ((a (b' + c'))+ d ) e' = (a (b' + c') + d) e'

## Slide 30: Canonical Forms
It is useful to specify Boolean functions in a form that:
  Allows comparison for equality.
  Has a correspondence to the truth tables
Canonical Forms in common usage:
  Sum of Minterms (SOM)
  Product of Maxterms (POM)

## Slide 31: Minterms
Minterms are AND terms with every variable present in either true or complemented form.
Given that each binary variable may appear normal (e.g., x) or complemented (e.g., ), there are 2n minterms for n variables.
Example: Two variables (X and Y)produce 2 x 2 = 4 combinations:
  (both normal)
  (X normal, Y complemented)
  (X complemented, Y normal)
  (both complemented)
Thus there are four minterms of two variables.
Y
X
XY
Y
X
Y
X
x

## Slide 32: Maxterms
Maxterms are OR terms with every variable in true or complemented form.
Given that each binary variable may appear normal (e.g., x) or complemented (e.g., x), there are 2n maxterms for n variables.
Example: Two variables (X and Y) produce 2 x 2 = 4 combinations:
  (both normal)
  (x normal, y complemented)
  (x complemented, y normal)
  (both complemented)
Y
X
+
Y
X
+
Y
X
+
Y
X
+

## Slide 33: Maxterms and Minterms
Examples: Two variable minterms and maxterms.
The index above is important for describing which variables in the terms are true and which are complemented.
Index | Minterm | Maxterm
0 | x y | x + y
1 | x y | x + y
2 | x y | x + y
3 | x y | x + y

## Slide 34: Purpose of the Index
The index for the minterm or maxterm, expressed as a binary number, is used to determine whether the variable is shown in the true form or complemented form.
For Minterms:
  “1” means the variable is “Not Complemented” and
  “0” means the variable is “Complemented”.
For Maxterms:
  “0” means the variable is “Not Complemented” and
  “1” means the variable is “Complemented”.

## Slide 35: Index Example in Three Variables
Example: (for three variables)
Assume the variables are called X, Y, and Z.
The standard order is X, then Y, then Z.
  Minterm 0, called m0 is .
  Maxterm 0, called M0 is (X + Y + Z).
  Minterm 6 ?
  Maxterm 6 ?
Z
Y
X
Notes: m6 = X Y Z’
M6 = (X’ + Y’ + Z)

## Slide 36: Index Examples – Four Variables
Index Binary Minterm Maxterm
i Pattern mi Mi
0 0000
1 0001
3 0011
5 0101
7 0111
10 1010
13 1101
15 1111
d
c
b
a
d
c
b
a
d
c
b
a
+
+
+
d
c
b
a
d
c
b
a
+
+
+
d
c
b
a
+
+
+
d
c
b
a
d
c
b
a
+
+
+
d
b
a
d
c
b
a
+
+
+
?
?
?
?
c
Notes: M1 = a + b + c + d’
m3 = a’ b’ c d
m7 = a’ b c d
M 13 = a’ + b’ + c + d’

## Slide 37: Minterm and Maxterm Relationship
y
x
y
·
x
+
=
y
x
y
x
×
=
+
y
x
M
2
+
=
y
x·
m
2
=
i
m
M
=
i
i
i
M
m
=

## Slide 38: Canonical Sum of Minterms
Any Boolean function can be expressed as a Sum of Minterms.
  For the function table, the minterms used are the terms corresponding to the 1's
  For expressions, expand all terms first to explicitly list all minterms. Do this by “ANDing” any term missing a variable v with a term ( ).
Example: Implement as a sum of minterms.
  First expand terms:
  Then distribute terms:
  Express as sum of minterms: f = m3 + m2 + m0
y
x
x
f
+
=
y
x
)
y
y
(
x
f
+
+
=
y
x
y
x
xy
f
+
+
=
v
v
+

## Slide 39: Example
x
y
f
+
=

## Slide 40: Shorthand SOM Form
From the previous example, we started with:
We ended up with:
F = m1+m4+m5+m6+m7
This can be denoted in the formal shorthand:
Note that we explicitly show the standard variables in order and drop the “m” designators.
C
B
A
F
+
=

## Slide 41: Canonical Product of Maxterms
Any Boolean Function can be expressed as a Product of Maxterms (POM).
  For the function table, the maxterms used are the terms corresponding to the 0's.
  Example: Convert to product of maxterms:
y
x
x
)
z
,
y
,
x
(
f
+
=
)
3
,
2
(
)
z
,
y
,
x
(
F
M
P
=
Express as POM: f = M2 · M3

## Slide 42: Standard Forms
Standard Sum-of-Products (SOP) form: equations are written as an OR of AND terms
Standard Product-of-Sums (POS) form: equations are written as an AND of OR terms
Examples:
  SOP:
  POS:
These “mixed” forms are neither SOP nor POS
B
C
B
A
C
B
A
+
+
C
·
)
C
B
(A
·
B)
(A
+
+
+
C)
(A
C)
B
(A
+
+
B)
(A
C
A
C
B
A
+
+

## Slide 43: Standard Sum-of-Products (SOP)
A Simplification Example:
Writing the minterm expression:
F = A B C + A B C + A B C + ABC + ABC
Simplifying:
F =
Simplified F contains 3 literals compared to 15 in minterm F
Notes: F = A’ B’ C + A (B’ C’ + B C’ + B’ C + B C)
= A’ B’ C + A (B’ + B) (C’ + C)
= A’ B’ C + A.1.1
= A’ B’ C + A
= B’C + A

## Slide 44: AND/OR Two-level Implementation of SOP Expression
The two implementations for F are shown below – it is quite apparent which is simpler!

## Slide 45: Circuit Optimization
Goal: To obtain the simplest implementation for a given function
Optimization is a more formal approach to simplification that is performed using a specific procedure or algorithm
Optimization requires a cost criterion to measure the simplicity of a circuit
Distinct cost criteria we will use:
  Literal cost (L)
  Gate input cost (G)
  Gate input cost with NOTs (GN)

## Slide 46: Literal Cost
D
Literal – a variable or it complement
Literal cost – the number of literal appearances in a Boolean expression corresponding to the logic circuit diagram
Examples:
  F = BD + A C + A L = 8
  F = BD + A C + A + AB L =
  F = (A + B)(A + D)(B + C + )( + + D) L =
  Which solution is best?
D
B
C
B
B
D
C
B
C
Notes: 2nd Literal Cost = 11
3rd Literal Cost = 10
The first solution is best

## Slide 48: F = BD + A B’C + AC’D’ - find L, G, GN

## Slide 49: Cost Criteria (continued)
Example 2:
F = A B C +
L = 6 G = 8 GN = 11
F = (A + )( + C)( + B)
L = 6 G = 9 GN = 12
Same function and same literal cost
But first circuit has better gate input count and better gate input count with NOTs
Select it!
B
C
A
A
B
C
F
C
B
F
A
B
C
A

## Slide 50: Simplify - F(A,B,C,D) = m2 + m3 + m6 + m7 + m10 +m11
Notes: F= A’C +B’C

## Slide 51: Boolean Function Optimization
Minimizing the gate input (or literal) cost of a (a set of) Boolean equation(s) reduces circuit cost.
We choose gate input cost.
Boolean Algebra and graphical techniques are tools to minimize cost criteria values.
Some important questions:
  When do we stop trying to reduce the cost?
  Do we know when we have a minimum cost?
Treat optimum or near-optimum cost functions for two-level (SOP and POS) circuits first.
Introduce a graphical technique using Karnaugh maps (K-maps, for short)

## Slide 52: Karnaugh Maps (K-map)
A K-map is a collection of squares
  Each square represents a minterm
  The collection of squares is a graphical representation of a Boolean function
  Adjacent squares differ in the value of one variable
  Alternative algebraic expressions for the same function are derived by recognizing patterns of squares
The K-map can be viewed as
  A reorganized version of the truth table
  A topologically-warped Venn diagram as used to visualize sets in algebra of sets

## Slide 53
Notes: Adjacent cell varies only one place either horizontal or vertical

## Slide 65: Two Variable Maps
A 2-variable Karnaugh Map:
  Note that minterm m0 and
  minterm m1 are “adjacent”
  and differ in the value of the
  variable y
  Similarly, minterm m0 and
  minterm m2 differ in the x variable.
  Also, m1 and m3 differ in the x variable as well.
  Finally, m2 and m3 differ in the value of the variable y
y = 0
y = 1
x = 0
m
0 =
m
1 =
x = 1
m
2 =
m
3 =
y
x
y
x
y
x
y
x

## Slide 66: Three Variable Maps
A three-variable K-map:
Where each minterm corresponds to the product terms:
Note that if the binary value for an index differs in one bit position, the minterms are adjacent on the K-Map
yz=00
yz=01
yz=11
yz=10
x=0
m0
m1
m3
m2
x=1
m4
m5
m7
m6
yz=00
yz=01
yz=11
yz=10
x=0
x=1
z
y
x
z
y
x
z
y
x
z
y
x
z
y
x
z
y
x
z
y
x
z
y
x

## Slide 67: Example: Combining Squares
Example: Let
Applying the Minimization Theorem three times:
Thus the four terms that form a 2 × 2 square correspond to the term "y".
y
=
z
y
yz
+
=
z
y
x
z
y
x
z
y
x
z
y
x
)
z
,
y
,
x
(
F
+
+
+
=
x
y
1
0
2
4
3
5
6
7
1
1
1
1
z

## Slide 68: Combining 1’s
By combining squares, we reduce number of literals in a product term, reducing the literal cost, thereby reducing the other two cost criteria
On a 3-variable K-Map:
  One square represents a minterm with three variables
  Two adjacent squares represent a product term with two variables
  Four “adjacent” terms represent a product term with one variable
  Eight “adjacent” terms is the function of all ones (no variables) = 1.

## Slide 69: Four Variable Terms
Four variable maps can have rectangles corresponding to:
  A single 1 = 4 variables, (i.e. Minterm)
  Two 1s = 3 variables,
  Four 1s = 2 variables
  Eight 1s = 1 variable,
  Sixteen 1s = zero variables (i.e. Constant "1")

## Slide 70: Four-Variable Map Simplification
)
8,10,13,15
2,4,5,6,7,
(0,
Z)
Y,
X,
F(W,
m
S
=

## Slide 71: Four-Variable Map Simplification
3,14,15
)
(3,4,5,7,9,1
Z)
Y,
X,
F(W,
m
S
=
Notes: F = W' X Y' + W' Y Z + WXY + WY'Z

## Slide 72: Fill a K-map from Boolean equation

## Slide 73: Don't Cares in K-Maps
Sometimes a function table or map contains entries for which it is known:
  the input values for the minterm will never occur, or
  The output value for the minterm is not used
In these cases, the output value need not be defined
Instead, the output value is defined as a “don't care”
By placing “don't cares” ( an “x” entry) in the function table or map, the cost of the logic circuit may be lowered.
Example 1: A logic function having the binary codes for the BCD digits as its inputs. Only the codes for 0 through 9 are used. The six codes, 1010 through 1111 never occur, so the output values for these codes are “x” to represent “don’t cares.”

## Slide 76: Sums of product Example
Find the optimum solution:
Notes: F' = B' D' + A' B
F = (B + D)(A + B')

## Slide 78: Example of Decimal to 7 segment display

## Slide 79: Verilog Example