## Slide 1: Sign Number and Addition, Subtraction

## Slide 2: How To Represent Signed Numbers
Plus and minus sign used for decimal numbers: 25 (or +25), -16, etc.
For computers, desirable to represent everything as bits.
Three types of signed binary number representations:
  signed magnitude,
  1’s complement,
  2’s complement.
In each case: left-most bit indicates sign: positive (0) or negative (1).

## Slide 3: Signed Magnitude
Consider signed magnitude:
000011002 = 1210
Sign bit
Magnitude
100011002 = -1210
Sign bit
Magnitude

## Slide 4: One’s Complement Representation
The one’s complement of a binary number involves inverting all bits.
  1’s comp of 00110011 is 11001100
  1’s comp of 10101010 is 01010101
To find negative of 1’s complement number take the 1’s complement.
000011002 = 1210
Sign bit
Magnitude
111100112 = -1210
Sign bit
Magnitude

## Slide 5: One’s complement

## Slide 6: Two’s Complement Representation
The two’s complement of a binary number involves inverting all bits and adding 1.
  2’s comp of 00110011 is 11001101
  2’s comp of 10101010 is 01010110
To find negative of 2’s complement number take the 2’s complement.
000011002 = 1210
Sign bit
Magnitude
111101002 = -1210
Sign bit
Magnitude

## Slide 7: Two’s Complement Representation

## Slide 8: Binary Addition
Binary addition is very simple.
This is best shown in an example of adding two binary numbers…
1 1 1 1 0 1
+ 1 0 1 1 1
---------------------
0
1
0
1
1
1
1
1
1
1
1
0
0
carries
Notes: Design state of art organization in 1990

## Slide 9: Binary Subtraction
We can also perform subtraction (with borrows in place of carries).
Let’s subtract (10111)2 from (1001101)2…
1 10
0 10 10 0 0 10
1 0 0 1 1 0 1
- 1 0 1 1 1
------------------------
1 1 0 1 1 0
borrows
Notes: Design state of art organization in 1990

## Slide 10: Binary Multiplication
Binary multiplication is much the same as decimal multiplication, except that the multiplication operations are much simpler…
1 0 1 1 1
X 1 0 1 0
-----------------------
0 0 0 0 0
1 0 1 1 1
0 0 0 0 0
1 0 1 1 1
-----------------------
1 1 1 0 0 1 1 0
Notes: Design state of art organization in 1990

## Slide 11: Addition
(123)4 + (23)4=(?)4
(35)5 + (23)5=(?)5

## Slide 12: Addition using 1’s complement
(12)10 + (23)10=(?)10

## Slide 13: Addition using 2’s complement
(12)10 + (23)10=(?)10

## Slide 14: Subtraction using 1’s complement
Start
Find 1’s complement of both number
Add both number(1’s complement)
Is carry generated
Add carry into the sum
Take 1’s complement and Add negative sign
Result is ready
No
Yes

## Slide 15: Subtraction using 1’s complement

## Slide 16: Subtraction using 2’s complement
Start
Find 2’s complement of both number
Add both number(2’s complement)
Is carry generated
Discard the carry
Take 2’s complement and Add negative sign
Result is ready
Yes
No

## Slide 17: Subtraction using 2’s complement

## Slide 18: Binary Coded Decimal (BCD)
The BCD code is the 8,4,2,1 code.
8, 4, 2, and 1 are weights
BCD is a weighted code
This code is the simplest, most intuitive binary code for decimal digits and uses the same powers of 2 as a binary number, but only encodes the first ten values from 0 to 9.
Example: 1001 (9) = 1000 (8) + 0001 (1)
Notes: Answer 1: 6
Answer 2: 1010, 1011, 1100, 1101, 1110, 1111

## Slide 19: Think
How many “invalid” code words are there?
What are the “invalid” code words?

## Slide 20: Uses of BCD
BCD enables fast conversions from denary to binary for applications such as pocket calculators.
Each digit on a calculator corresponds directly to a four-bit block in BCD.

## Slide 21: Excess 3 Code and 8, 4, –2, –1 Code
What interesting property is common to these two codes?
Decimal | Excess 3 | 8, 4, –2, –1
0 | 0011 | 0000
1 | 0100 | 0111
2 | 0101 | 0110
3 | 0110 | 0101
4 | 0111 | 0100
5 | 1000 | 1011
6 | 1001 | 1010
7 | 1010 | 1001
8 | 1011 | 1000
9 | 1100 | 1111
Notes: Answer: Both of these codes have the property that the codes for 0 and 9, 1 and 8, etc. can be obtained from each other by replacing the 0’s with the 1’s and vice-versa in the code words. Such a code is sometimes called a complement code.

## Slide 22: Warning: Conversion or Coding?
Do NOT mix up conversion of a decimal number to a binary number with coding a decimal number with a BINARY CODE.
1310 = 11012 (This is conversion)
13  0001|0011 (This is coding)

## Slide 23: BCD Addition
Consider the following BCD operation
  Decimal: Add 4 + 1
  Covert to binary 0 1 0 0
  And 0 0 0 1
  Getting 0 1 0 1
  Which is still a BCD representation of a decimal digit

## Slide 24: Another
A second example
  3 0 0 1 1
  +3 0 0 1 1
  Getting 6 or 0 1 1 0
  And in range and a BCD digit representation

## Slide 25: BCD Arithmetic
Given a BCD code, we use binary arithmetic to add the digits:
8
1000
Eight
+5
+0101
Plus 5
13
1101
is 13 (> 9)
Note that the result is MORE THAN 9, so must be represented by two digits!
To correct the digit, adding 6.
8
1000
Eight
+5
+0101
Plus 5
13
1101
is 13 (> 9)
+0110
so add 6
carry = 1
0011
leaving 3 + cy
0001 | 0011
Final answer (two digits)
If the digit sum is > 9, add one to the next significant digit

## Slide 26: BCD Addition Example
Add 2905BCD to 1897BCD showing carries and digit corrections.
0001 1000 1001 0111
+ 0010 1001 0000 0101
0
Notes: 1 1 1 0
0001 1000 1001 0111
+ 0010 1001 0000 0101
0100 10010 1010 1100
+ 0000+ 0110+ 0110+ 0110
0100 1000 0000 0010

## Slide 27: Number of Bits Required
Given M elements to be represented by a binary code, the minimum number of bits, n, needed, satisfies the following relationships:
    2n ³ M > 2(n – 1)
    n = log2 M
    where x , called the ceiling function, is the integer greater than or equal to x.
Example: How many bits are required to represent decimal digits with a binary code?
Notes: M = 10
Therefore n = 4 since:
24 =16 is  10 > 23 = 8
and the ceiling function for log2 10 is 4.

## Slide 28: Number of Elements Represented
Given n digits in radix r, there are rn distinct elements that can be represented.
But, you can represent m elements, m < rn
Examples:
  You can represent 4 elements in radix r = 2 with n = 2 digits: (00, 01, 10, 11).
  You can represent 4 elements in radix r = 2 with n = 4 digits: (0001, 0010, 0100, 1000).
  This second code is called a "one hot" code.