## Slide 1: Sign Number and Addition, Subtraction

## Slide 2: How To Represent Signed Numbers
Plus and minus sign used for decimal numbers: 25 (or +25), -16, etc.
For computers, desirable to represent everything as bits.
Three types of signed binary number representations:
  signed magnitude,
  1’s complement,
  2’s complement.
In each case: left-most bit indicates sign: positive (0) or negative (1).

## Slide 3: Signed Magnitude
Consider signed magnitude:
000011002 = 1210
Sign bit
Magnitude
100011002 = -1210
Sign bit
Magnitude

## Slide 4: One’s Complement Representation
The one’s complement of a binary number involves inverting all bits.
  1’s comp of 00110011 is 11001100
  1’s comp of 10101010 is 01010101
To find negative of 1’s complement number take the 1’s complement.
000011002 = 1210
Sign bit
Magnitude
111100112 = -1210
Sign bit
Magnitude

## Slide 5: One’s complement

## Slide 6: Two’s Complement Representation
The two’s complement of a binary number involves inverting all bits and adding 1.
  2’s comp of 00110011 is 11001101
  2’s comp of 10101010 is 01010110
To find negative of 2’s complement number take the 2’s complement.
000011002 = 1210
Sign bit
Magnitude
111101002 = -1210
Sign bit
Magnitude

## Slide 7: Two’s Complement Representation

## Slide 8: Binary Addition
Binary addition is very simple.
This is best shown in an example of adding two binary numbers…
1 1 1 1 0 1
+ 1 0 1 1 1
---------------------
0
1
0
1
1
1
1
1
1
1
1
0
0
carries
Notes: Design state of art organization in 1990

## Slide 11: Binary Subtraction
We can also perform subtraction (with borrows in place of carries).
Let’s subtract (10111)2 from (1001101)2…
1 10
0 10 10 0 0 10
1 0 0 1 1 0 1
- 1 0 1 1 1
------------------------
1 1 0 1 1 0
borrows
Notes: Design state of art organization in 1990

## Slide 12: Binary Multiplication
Binary multiplication is much the same as decimal multiplication, except that the multiplication operations are much simpler…
1 0 1 1 1
X 1 0 1 0
-----------------------
0 0 0 0 0
1 0 1 1 1
0 0 0 0 0
1 0 1 1 1
-----------------------
1 1 1 0 0 1 1 0
Notes: Design state of art organization in 1990

## Slide 13: Addition
(123)4 + (23)4=(?)4
(35)5 + (23)5=(?)5

## Slide 14: Addition using 1’s complement
(12)10 + (23)10=(?)10

## Slide 15: Addition using 2’s complement
(12)10 + (23)10=(?)10

## Slide 16: Subtraction using 1’s complement
Start
Find 1’s complement of both number
Add both number(1’s complement)
Is carry generated
Add carry into the sum
Take 1’s complement and Add negative sign
Result is ready
No
Yes

## Slide 17: Subtraction using 1’s complement

## Slide 18: Subtraction using 2’s complement
Start
Find 2’s complement of both number
Add both number(2’s complement)
Is carry generated
Discard the carry
Take 2’s complement and Add negative sign
Result is ready
Yes
No

## Slide 19: Subtraction using 2’s complement

## Slide 20: Number of Bits Required
Given M elements to be represented by a binary code, the minimum number of bits, n, needed, satisfies the following relationships:
    2n ³ M > 2(n – 1)
    n = log2 M
    where x , called the ceiling function, is the integer greater than or equal to x.
Example: How many bits are required to represent decimal digits with a binary code?
Notes: M = 10
Therefore n = 4 since:
24 =16 is  10 > 23 = 8
and the ceiling function for log2 10 is 4.

## Slide 21: Number of Elements Represented
Given n digits in radix r, there are rn distinct elements that can be represented.
But, you can represent m elements, m < rn
Examples:
  You can represent 4 elements in radix r = 2 with n = 2 digits: (00, 01, 10, 11).
  You can represent 4 elements in radix r = 2 with n = 4 digits: (0001, 0010, 0100, 1000).
  This second code is called a "one hot" code.